## Slide 1: 6D Object Pose Estimation and 2D Object Outline Extraction for Robotic Grasping
Daniel Sawyer
Tian Tan

## Slide 2: Presentation topics
Detectron tutorial
Vision for object 6D pose estimation
Vision for grasp tuning

## Slide 3: The Problem
Getting a robot to pick items up (grasp them) in a dynamic environment
A multilevel problem that requires multiple systems working in unison
Ability to run inference remotely since the hardware required will not be available directly on the robot
Mask R-CNN tutorial

## Slide 4: Our Solution
Detectron’s Mask R-CNN algorithm in order to get semantic segmentation and object classification with localization
DenseFusion 6 DOF pose estimation algorithm
Grasp Tuning
Use HTTP GET/POST in order to run both networks and send/receive information to/from them remotely
Mask R-CNN tutorial

## Slide 5: DenseFusion 6 DoF Pose Estimation
In order to grasp objects, we need their 6 DoF pose which includes 7 values
Estimates X, Y, Z coordinates along with the 4 Quaternion values
Gives orientation and position in order to grasp object
Needs object localization and mask in order to work properly
Mask R-CNN tutorial

## Slide 6: What is Detectron?
Detectron is Facebook AI Research’s (FAIR) software system that implements state-of-the-art object detection algorithms
Inlcudes newest versions of Faster R-CNN, Mask R-CNN, and DensePose Human Pose Estimation
Built using Python and powered using Caffe2 which is now rolled into PyTorch
Allows use of multiple algorithms with different configuration files, has many pretrained models available, and is well documented so getting it up and running is fairly easy
Mask R-CNN tutorial

## Slide 7: Why Detectron?
In order to run our DenseFusion 6 DoF pose estimation we must first have an RoI (Region of Interest) of the object (bounding box), object label, and finally an object mask in order to estimate the pose
Has newest and easiest to use version of Mask R-CNN
Fast and comparatively easy to get up and running
Works with newest version of PyTorch, no going around searching/installing deprecated libraries
Mask R-CNN tutorial

## Slide 8: Implement Mask R-CNN using Detectron
Implemented using Python 3.7, PyTorch 1.0.1, and CUDA 10
Detectron Model Zoo, all models using pretrained ImageNet backbone
Setting up Conda Environment suitable for Detectron
Set up config file and choose a pretrained model
Training using your own data
Mask R-CNN tutorial

## Slide 9: Implement Mask R-CNN using Detectron
Github links: https://github.com/facebookresearch/Detectron, https://github.com/sawyermade/Detectron
Live demo
Explanation of HTTP subsystem for transferring information
How to keep networks loaded and awaiting HTTP POST which runs inference much quicker than loading the network every time it is needed
Mask R-CNN tutorial

## Slide 10: Vision for Grasp Tuning
Purpose
  Reduce grasp error
Vision problem statement
  From single-view RGB image find
  how to move the gripper so that
  the object can be grasped at a
  good location.
Vision for Grasp Tuning

## Slide 11: Vision for Grasp Tuning
Approach
  Mask R-CNN detect object mask
  Object 2D outline extraction from object mask
  Calculate pixel-wise normal of the outline
  Calculate grasp features and adjust robot gripper
Vision for Grasp Tuning
Detect outline
Find contact region & outline normal
Valid contact?
Current gripper pose
Continue grasp motion
Adjust grasp motion
Calculate grasp features
YES
NO

## Slide 12: Vision for Grasp Tuning
Mask R-CNN object mask detection result
Vision for Grasp Tuning

## Slide 13: Vision for Grasp Tuning
Object outline extraction
  For each row of the image find the two outline
  points of each continuous region of the mask
Pixel-wise normal
  Find the normal of the vector of neighbors
  Choose the normal direction based on pixel position
  relative to the center of the mask
  - Average the normal of neighbors
Vision for Grasp Tuning

## Slide 14: Vision for Grasp Tuning
Object outline and normal extraction results
Vision for Grasp Tuning

## Slide 15: Vision for Grasp Tuning
Grasp features
Vision for Grasp Tuning

## Slide 16: Vision for Grasp Tuning
Grasp features and gripper adjustment
  A 3D grasp is defined by 6 parameters(x, y, z, roll, pitch, yaw) also known as the 6 degrees of freedom. Due to the limitation of single-view RGB image we can tune only 3 of them and they are x, y and roll.
  Grasp feature for adjustment of gripper x(left-right)
  Grasp feature for adjustment of gripper y(up-down)
  Grasp feature for adjustment of gripper roll(rotation about its z-axis)
  is positive when the normal is above horizontal, negative if below.
Vision for Grasp Tuning

## Slide 17: Vision for Grasp Tuning
Grasp features and gripper adjustment results
Vision for Grasp Tuning